YD647 User Manual for

HiCo Magstrip Read/Encoder

Software install:

- Double-click on the package ---- Choose install path---- Click on the desktop shortcut

- Equipment use usb interface, pay attention to the first to install usb to RS232driver

Magnetic stripe reader and writer software

Double-click on the package:

Double-click setup.exe

The main window :

Open the device menu

Serial Port :

Users only need to set the Serial Port,，The other default

How to set the correct Serial Port:

PC transfer and magnetic stripe card reader with USB serial communication mode

1：install usb to RS232driver

2：Plug in the device, the computer is assigned to a virtual port devices

3：View the virtual port is what port

Right-click the "my computer"-----"Properties"------switched to the "hardware" tab----click "Device Manager"-------found "ports (COM and LPT)"

Operation type of card

# Text boxes

Operator Message

Action type menu (read/write/erase)

Select track

Track data

High and low coercivity selection

File Browse dialog box

Read from File Open

Auto increment NO.

Write Track Auto increment

Baud rate

Serial Port

Computer is  assigned to the device "COM3"

Read card

Write card

Erase card

Reset

Device parameter settings